Calio Z High-efficiency Circulator Pump

Maintenance-free high-efficiency glandless twin pump, non-overloading synchronous motor with ECM technology, integrated continuously variable differential pressure control. Energy efficiency index (EEI) exceeds the ErP 2015 requirements. For heating and air-conditioning applications.

Operating modes:

- Constant-pressure control

- Proportional-pressure control

- Eco Mode with dynamic differential pressure setpoint adjustment

- Boost Mode (open-loop control)

- Temperature-governed differential pressure control

Functions:

- Dual-pump operation, pump changeover after 24 hours runtime of a pump

- Peak load operation

- Redundancy by automatic start-up of the stand-by pump in the event of a duty pump failure

- Operating mode set manually or via Modbus

- Setpoint settings 0 - 100 % in increments of 1 %

- Setpoint for differential pressure set manually or via external 0 - 10 VDC analog signal or via Modbus

- Setpoint for rotational speed (open-loop control) set manually or via external 0 - 10 VDC analog signal or via Modbus

- Remote monitoring and control of pump via Modbus

- Control panel with integrated symbols, showing the operating mode and, in alternation, the electrical input power, flow rate and head

- Error codes indicated on the display

- Automatic setback operation, can be disabled

- Automatic venting

- Soft start with limitation of starting current

- Deblocking function

- Integrated motor protection function

- Characteristic curve monitoring by means of max./min. flow limit

- Energy meter / flow rate meter

- Dynamic Control

Communication interfaces integrated in the pump:

- Terminal pair for Modbus RTU interface

- Terminal pair for external analog 0 - 10 V DC signal

- Terminal pair for external ON/OFF of the pump

- Terminal pair for twin pump operation

- Configurable general fault message relay (changeover contact, per drive)

- Configurable "in operation" message relay (changeover contact, per drive)

Operating data

Fluid handled:

Flow rate:

Head:

Fluid temperature:

Permissible fluid temperature min./max.: -10 to 110 ºC

Maximum operating pressure:

Max. ambient temperature: 40 °C

Motor/electronics

Energy efficiency index (EEI):

Electromagnetic compatibility

Interference emissions P1 < 400W: EN 55014-1, EN 61000-3-2, EN 61000-3-3

Interference emissions P1 > 400W: EN 61800-3

Interference immunity P1 < 400W: EN 55014-2

Interference immunity P1 > 400W: EN 61800-3

Power supply: 1~ 230 V AC +/- 10 %, 50/60 Hz

Power input P1:

Speed min. ... max.:

Current input max.:

Enclosure IPX4D

Materials

Pump casing: grey cast iron with cathodic electrocoating (EN-GJL-200)

Impeller: plastic with glass fibre content (PSU-GF30)

Pump shaft: stainless steel 1.4034

Bearings: ceramics/carbon

Mating dimensions

Pipe connection:

Overall length:

Purchase order information

Approx. net weight:

Make: KSB

Type: Calio Z

Material price group: 54

Material number

Accessories

BACnet MS/TP communication module

Spacers

Pipe unions

Calio Z Typical Tender

1157.525/07-EN

Subject to technical modification without prior notice.

18 November 2022