| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ20.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 28.9 l/s (104 m3/h) Head up to 30 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 20.1 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 411 kg Make KSB Size Compacta UZ20.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ20.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 28.9 l/s (104 m3/h) Head up to 30 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 20.1 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 486 kg Make KSB Size Compacta UZ20.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ21.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 32.8 l/s (118 m3/h) Head up to 34.5 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 20.1 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 411 kg Make KSB Size Compacta UZ21.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ21.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 32.8 l/s (118 m3/h) Head up to 34.5 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 20.1 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 486 kg Make KSB Size Compacta UZ21.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ22.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 36.9 l/s (133 m3/h) Head up to 40 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 27.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 425 kg Make KSB Size Compacta UZ22.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ22.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 36.9 l/s (133 m3/h) Head up to 40 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 27.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 500 kg Make KSB Size Compacta UZ22.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ23.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 40.3 l/s (145 m3/h) Head up to 47 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 18.5 kW Nom. motor current IN,Y/D 33.9 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 469 kg Make KSB Size Compacta UZ23.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ23.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 40.3 l/s (145 m3/h) Head up to 47 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 18.5 kW Nom. motor current IN,Y/D 33.9 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 544 kg Make KSB Size Compacta UZ23.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ24.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 42.3 l/s (154 m3/h) Head up to 51 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 38.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 499 kg Make KSB Size Compacta UZ24.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

|  |  | KSB waste water and sewage lifting unit Compacta UZ24.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 42.3 l/s (154 m3/h) Head up to 51 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |
| --- | --- | --- | --- | --- |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 38.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 574 kg Make KSB Size Compacta UZ24.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ25.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 32.8 l/s (118 m3/h) Head up to 57 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 26 kW Nom. motor current IN,Y/D 45.5 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 527 kg Make KSB Size Compacta UZ25.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ25.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 32.8 l/s (118 m3/h) Head up to 57 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 26 kW Nom. motor current IN,Y/D 45.5 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 602 kg Make KSB Size Compacta UZ25.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ26.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 23.1 l/s (83 m3/h) Head up to 62.5 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 26 kW Nom. motor current IN,Y/D 45.5 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 527 kg Make KSB Size Compacta UZ26.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ26.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 23.1 l/s (83 m3/h) Head up to 62.5 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 80-253 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 26 kW Nom. motor current IN,Y/D 45.5 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 602 kg Make KSB Size Compacta UZ26.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ27a.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 38.5 l/s (140 m3/h) Head up to 26 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 100-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 27.7 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 427 kg Make KSB Size Compacta UZ27a.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ27a.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 38.5 l/s (140 m3/h) Head up to 26 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 100-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 27.7 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 502 kg Make KSB Size Compacta UZ27a.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ27.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 41.5 l/s (146 m3/h) Head up to 29.5 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 100-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 18.5 kW Nom. motor current IN,Y/D 33.9 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 465 kg Make KSB Size Compacta UZ27.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ27.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 41.5 l/s (146 m3/h) Head up to 29.5 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 100-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 18.5 kW Nom. motor current IN,Y/D 33.9 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 540 kg Make KSB Size Compacta UZ27.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ28.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 42.5 l/s (154 m3/h) Head up to 33 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 100-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 38.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 495 kg Make KSB Size Compacta UZ28.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ28.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 42.5 l/s (153 m3/h) Head up to 33 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 100-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 38.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 570 kg Make KSB Size Compacta UZ28.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ29.450 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 44.5 l/s (160 m3/h) Head up to 36 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 100-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 38.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 495 kg Make KSB Size Compacta UZ29.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta UZ29.900 D Floodable ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 44.5 l/s (160 m3/h) Head up to 36 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two submersible motor pumps, type Amarex KRT F 100-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, three-phase motor with integrated overload protection, enclosure IP68, non-explosion-proof D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by thermal circuit breaker and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 38.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 570 kg Make KSB Size Compacta UZ29.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF30.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 28.6 l/s (103 m3/h) Head up to 14.6 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 10.5 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 327 kg Make KSB Size Compacta ZF30.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF30.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 28.6 l/s (103 m3/h) Head up to 14.6 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 10.5 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 402 kg Make KSB Size Compacta ZF30.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF31.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 30 l/s (108 m3/h) Head up to 18 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 14.6 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 333 kg Make KSB Size Compacta ZF31.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF31.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 41.7 l/s (150 m3/h) Head up to 33 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 14.6 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 408 kg Make KSB Size Compacta ZF31.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF32.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 31.7 l/s (114 m3/h) Head up to 22 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 357 kg Make KSB Size Compacta ZF32.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF32.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 31.7 l/s (114 m3/h) Head up to 22 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 432 kg Make KSB Size Compacta ZF32.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF33.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 33.3 l/s (120 m3/h) Head up to 26.6 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 357 kg Make KSB Size Compacta ZF33.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF33.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 33.3 l/s (120 m3/h) Head up to 26.6 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 432 kg Make KSB Size Compacta ZF33.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF34.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 35.3 l/s (127 m3/h) Head up to 30.6 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 29.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 383 kg Make KSB Size Compacta ZF34.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF34.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 35.3 l/s (127 m3/h) Head up to 30.6 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 29.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 458 kg Make KSB Size Compacta ZF34.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF35.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 37.2 l/s (134 m3/h) Head up to 34.8 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 29.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 383 kg Make KSB Size Compacta ZF35.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF35.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 37.2 l/s (134 m3/h) Head up to 34.9 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 29.4 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 458 kg Make KSB Size Compacta ZF35.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF36.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 39.2 l/s (141 m3/h) Head up to 39.4 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 18.5 kW Nom. motor current IN,Y/D 35.6 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 426 kg Make KSB Size Compacta ZF36.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF36.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 39.2 l/s (141 m3/h) Head up to 39.4 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 18.5 kW Nom. motor current IN,Y/D 35.6 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 498 kg Make KSB Size Compacta ZF36.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF37.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 41.4 l/s (149 m3/h) Head up to 43.8 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 41.2 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 535 kg Make KSB Size Compacta ZF37.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF37.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 41.4 l/s (149 m3/h) Head up to 43.8 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 41.2 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 610 kg Make KSB Size Compacta ZF37.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF38.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 43.2 l/s (155.5 m3/h) Head up to 47.8 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 41.2 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 535 kg Make KSB Size Compacta ZF37.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF38.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 43.2 l/s (155.5 m3/h) Head up to 47.8 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-216 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 22 kW Nom. motor current IN,Y/D 41.2 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 610 kg Make KSB Size Compacta ZF37.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF40.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 23.5 l/s (84.5 m3/h) Head up to 6.9 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 3.0 kW Nom. motor current IN 6.2 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 327 kg Make KSB Size Compacta ZF40.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF40.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 23.5 l/s (84.5 m3/h) Head up to 6.9 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 3.0 kW Nom. motor current IN 6.2 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 402 kg Make KSB Size Compacta ZF40.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF41.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 27.8 l/s (100 m3/h) Head up to 8.9 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 4.0 kW Nom. motor current IN 8.6 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 345 kg Make KSB Size Compacta ZF41.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF41.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 27.8 l/s (100 m3/h) Head up to 8.9 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 4.0 kW Nom. motor current IN 8.6 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 420 kg Make KSB Size Compacta ZF41.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF42.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 32.8 l/s (118 m3/h) Head up to 10.9 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 11.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 389 kg Make KSB Size Compacta ZF42.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF42.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 32.8 l/s (118 m3/h) Head up to 10.9 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 11.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 464 kg Make KSB Size Compacta ZF42.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF43.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 39 l/s (140.5 m3/h) Head up to 15.2 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 395 kg Make KSB Size Compacta ZF43.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF43.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 39 l/s (140.5 m3/h) Head up to 15.2 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 470 kg Make KSB Size Compacta ZF43.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF44.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 45.3 l/s (163 m3/h) Head up to 17.9 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 395 kg Make KSB Size Compacta ZF44.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF44.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 45.3 l/s (163 m3/h) Head up to 17.9 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 470 kg Make KSB Size Compacta ZF44.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF45.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 36.8 l/s (132.5 m3/h) Head up to 21.7 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-251 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22.8 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 449 kg Make KSB Size Compacta ZF45.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF45.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 36.8 l/s (132.5 m3/h) Head up to 21.7 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-251 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22.8 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 524 kg Make KSB Size Compacta ZF45.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF46.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 37 l/s (133 m3/h) Head up to 24.2 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-251 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 30.1 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 509 kg Make KSB Size Compacta ZF46.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF46.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 37 l/s (133 m3/h) Head up to 24.2 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-251 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 15 kW Nom. motor current IN,Y/D 30.1 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 584 kg Make KSB Size Compacta ZF46.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF47.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 25.6 l/s (92 m3/h) Head up to 4.6 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 1.5 kW Nom. motor current IN 3.6 A Speed 960 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 319 kg Make KSB Size Compacta ZF47.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF47.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 25.6 l/s (92 m3/h) Head up to 4.6 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 1.5 kW Nom. motor current IN 3.6 A Speed 960 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 394 kg Make KSB Size Compacta ZF47.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF48.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 33.9 l/s (122 m3/h) Head up to 7.9 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 3.0 kW Nom. motor current IN 6.6 A Speed 960 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 363 kg Make KSB Size Compacta ZF48.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF48.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 33.9 l/s (122 m3/h) Head up to 7.9 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 3.0 kW Nom. motor current IN 6.6 A Speed 960 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 438 kg Make KSB Size Compacta ZF48.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF49.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 47.8 l/s (172 m3/h) Head up to 10.5 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 4.0 kW Nom. motor current IN 8.6 A Speed 960 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 463 kg Make KSB Size Compacta ZF49.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF49.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 47.8 l/s (172 m3/h) Head up to 10.5 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 100-254 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 80 mm Motor rating P2 4.0 kW Nom. motor current IN 8.6 A Speed 960 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 438 kg Make KSB Size Compacta ZF49.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK50.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 35.6 l/s (128 m3/h) Head up to 15.1 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 80-250 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 11.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 381 kg Make KSB Size Compacta ZK50.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK50.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 35.6 l/s (128 m3/h) Head up to 15.1 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 80-250 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 11.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 456 kg Make KSB Size Compacta ZK50.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK51.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 40.1 l/s (144.5 m3/h) Head up to 17 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 80-250 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 11.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 381 kg Make KSB Size Compacta ZK51.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK51.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 40.1 l/s (144.5 m3/h) Head up to 17 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 80-250 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 11.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 456 kg Make KSB Size Compacta ZK51.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK52.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 44.7 l/s (161 m3/h) Head up to 18.9 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 80-250 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 383 kg Make KSB Size Compacta ZK52.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK52.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 44.7 l/s (161 m3/h) Head up to 18.9 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 80-250 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 458 kg Make KSB Size Compacta ZK52.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK53.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 48.4 l/s (174 m3/h) Head up to 20.8 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 80-250 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 383 kg Make KSB Size Compacta ZK53.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK53.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 48.4 l/s (174 m3/h) Head up to 20.8 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 80-250 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 458 kg Make KSB Size Compacta ZK53.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK54.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 58.9 l/s (212 m3/h) Head up to 14.1 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 100-254 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 11.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 389 kg Make KSB Size Compacta ZK54.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK54.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 58.9 l/s (212 m3/h) Head up to 14.1 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 100-254 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 11.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 464 kg Make KSB Size Compacta ZK54.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK55.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 69.2 l/s (249 m3/h) Head up to 16.2 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 100-254 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 415 kg Make KSB Size Compacta ZK55.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK55.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 69.2 l/s (249 m3/h) Head up to 16.2 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 100-254 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 490 kg Make KSB Size Compacta ZK55.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK56.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 74.5 l/s (268 m3/h) Head up to 17.8 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 100-254 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 415 kg Make KSB Size Compacta ZK56.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZK56.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 74.5 l/s (268 m3/h) Head up to 17.8 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 100, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc K 100-254 with closed multi-channel impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 71 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 15.0 A Speed 1450 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 490 kg Make KSB Size Compacta ZK56.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF60.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 20 l/s (72 m3/h) Head up to 15.4 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 3.0 kW Nom. motor current IN,Y/D 5.9 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 269 kg Make KSB Size Compacta ZF60.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF60.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 20 l/s (72 m3/h) Head up to 15.4 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 3.0 kW Nom. motor current IN,Y/D 5.9 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 344 kg Make KSB Size Compacta ZF60.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF61.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 20.4 l/s (73.5 m3/h) Head up to 18.5 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 4.0 kW Nom. motor current IN,Y/D 8.0 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 287 kg Make KSB Size Compacta ZF61.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF61.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 20.4 l/s (73.5 m3/h) Head up to 18.5 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 4.0 kW Nom. motor current IN,Y/D 8.0 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 362 kg Make KSB Size Compacta ZF61.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF62.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 21.5 l/s (77.5 m3/h) Head up to 21.8 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 4.0 kW Nom. motor current IN,Y/D 8.0 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 287 kg Make KSB Size Compacta ZF62.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF62.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 21.5 l/s (77.5 m3/h) Head up to 21.8 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 4.0 kW Nom. motor current IN,Y/D 8.0 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method DOL Electrical connection - Motor connection cable 10 m Weight (approx.) 362 kg Make KSB Size Compacta ZF62.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF63.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 22.2 l/s (80 m3/h) Head up to 25.6 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 10.5 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 331 kg Make KSB Size Compacta ZF63.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF63.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 22.2 l/s (80 m3/h) Head up to 25.6 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 5.5 kW Nom. motor current IN,Y/D 10.5 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 406 kg Make KSB Size Compacta ZF63.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF64.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 23.3 l/s (84 m3/h) Head up to 29.2 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 14.9 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 337 kg Make KSB Size Compacta ZF64.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF60.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 23.3 l/s (84 m3/h) Head up to 29.2 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 14.9 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 412 kg Make KSB Size Compacta ZF64.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF65.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 24.7 l/s (89 m3/h) Head up to 33.3 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 14.6 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 337 kg Make KSB Size Compacta ZF65.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF65.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 24.7 l/s (89 m3/h) Head up to 33.3 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 7.5 kW Nom. motor current IN,Y/D 14.6 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 412 kg Make KSB Size Compacta ZF65.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF66.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 26.1 l/s (94 m3/h) Head up to 36.9 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 361 kg Make KSB Size Compacta ZF66.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF66.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 26.1 l/s (994 m3/h) Head up to 36.9 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 436 kg Make KSB Size Compacta ZF66.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF67.450 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D One collecting tank made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 27.1 l/s (97.5 m3/h) Head up to 40.7 m - Vol. content 450 l - Dimensions 1015 x 840 x 900 mm - Inlet connections Horizontal 2 x DN 150 1 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 361 kg Make KSB Size Compacta ZF67.450 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | KSB waste water and sewage lifting unit Compacta ZF67.900 D Ready-to-connect dual-pump unit acc. to EN 12050-1, comprising: D Two collecting tanks made of impact-resistant plastic with hand hole cover, gas-, water- and odour-proof - Application range Flow rate up to 27.1 l/s (97.5 m3/h) Head up to 40.7 m - Vol. content 900 l - Dimensions 1015 x 1700 x 900 mm - Inlet connections Horizontal 2 x DN 150 2 x DN 200/150, graded, inlet nozzle level 700 mm incl. flexible hose connection for DN 150 - Discharge connection DN 80, incl. flexible hose connection - Vent connection DN 70, incl. flexible hose connection - Drain connection DN 40, incl. flexible hose connection (hand diaphragm pump) D Two waste water pumps, type Sewabloc F 80-215 with free-flow impeller GG, 2 mechanical seals SiC/SiC with barrier fluid reservoir, standardised three-phase motor with integrated overload protection, enclosure IP55, non-explosion-proof Suitable for S1 mode of operation, non-floodable D Material variant "C" for aggressive fluids on request *) D One analog sensor for direct level detection |  |  |

*)	Delete as applicable

| Cons. No. | Quantity | Item | Unit price | Total |
| --- | --- | --- | --- | --- |
|  |  | D One LevelControl Basic 2 control unit made by KSB - Self-adjusting, fully automatic control unit - Ready to connect - Numerical display with status indication (traffic light) and navigation keys - Indication of fill level - Indication of operating data - Analog level detection with sensor monitoring - Dynamic adjustment of switching points - Control unit in sturdy sheet steel housing - Version with integrated master switch - Manual-0-automatic selector switch - Indicator lamps for operation, fault and high water - Pump protection by PTC analysis and motor protection switch - Integrated alarm buzzer - Battery-backed mains-independent alarm - Two inputs for external fault signalling and remote acknowledgement - General fault message or volt-free "system operational" message - Equal distribution of pump operating hours ensured by automatic pump changeover - Parameterisable service intervals - Diagnostic and message functions - Numerous additional functions (e.g. monitoring of supply voltage, intelligent system monitoring and many more) Flow rate ...............m3/h...............l/s Head ...............m Temperature (fluid handled) up to 40 °C, for short periods up to 65 °C (5 minutes) Free passage 76 mm Motor rating P2 11 kW Nom. motor current IN,Y/D 22 A Speed 2900 rpm Supply voltage 3/N/PE, 400 V, 50 Hz Starting method star-delta Electrical connection - Motor connection cable 10 m Weight (approx.) 436 kg Make KSB Size Compacta ZF67.900 D Electrical installations must be protected against overvoltage (compulsory since 14 December 2018) (see DIN VDE 0100-443 (IEC60364-4-44:2007/A1:2015, modified) and DIN VDE 0100-534 (IEC 60364-5-53:2001/ A2:2015, modified). The lightning protection concept must be provided by the operator or by a suitable supplier contracted by the operator. Surge protective devices can be offered for the control units on request. |  |  |

2317.527/05-EN../..07.11.2019

2317.527/05-EN../..07.11.2019

Subject to technical modification without prior notice.

Subject to technical modification without prior notice.

*)	Delete as applicable