AmaDrainer 3

Vertical, single-stage, fully floodable submersible motor pump in close-coupled design, either with integrated level switch for automatic control or controlled via an external control unit

Function:

Submersible waste water pump for handling

·	Slightly contaminated waste water (up to 70 °C max.)

·	Wash water (for short periods of t <= 3 minutes up to 90 °C max.)

·	Waste water without faeces

·	Seepage water, river water, lake water and groundwater

In variant C also

·	Seawater

·	Brackish water

·	And water containing salt (up to 20 °C max.)

Features:

-	Ready-to-connect submersible motor pump in plastic casing, enclosure IP68

-	Integrated sensor unit for flexible use with and without control unit by simply locking the float switch in continuously ON position

-	All sizes available in material variant for aggressive fluids

-	Sizes 301, 303 only:

o	Integrated low water level intake option for residual water level as low as 2 mm

-	Sizes 301, 303, 322 only:

o	Integrated swing check valve

-	Size 322 only:

o	Integrated cleaning of pump sump (optional)

-	Maximum immersion depth of 2 m

Operating data:

Fluid handled:

Flow rate Q:

Head H:

Permissible fluid temperature: ≤ 70 °C in continuous operation, for a short time (t ≤ 3 minutes) up to 90 °C max.

Free passage – 301, 303: 10 mm

Free passage – 322: 18 mm

Free passage – 354: 35 mm

Drive:

Supply voltage:

Frequency:

Nominal power P1:

Motor rating P2:

Nominal current:

Monitoring / open-loop control / closed-loop control:

Pump controlled via integrated float switch or LevelControl Basic 2

Materials:

Pump casing: polypropylene, 30 % glass fibre reinforced

Discharge casing: polypropylene, 30 % glass fibre reinforced

Casing cover: polypropylene, 20 % talcum (PP-TS 20)

Shaft - material variant A: AISI 431

Shaft - material variant C:

-	Drive end: AISI 431

-	Pump end: AISI 316L

Impeller - sizes 301, 303: Noryl GNF2

Impeller - sizes 322, 354: polyamide

Automatic switchgear system: polypropylene

Motor housing - material variant A: AISI 304

Motor housing - material variant C: AISI 316L

Dimensions and connections:

Discharge side - 301, 303, 322: Rp 1 ¼“

Discharge side - 354: G 1 ½“

Purchase order information:

Make: KSB

Type series / size:

Material price group:

Weight:

Material number:

Typical tender for AmaDrainer 3

2332.521/03-EN

Subject to technical modification without prior notice

07 Octobre 2021