Amarex

KSB submersible motor pump for wastewater applications, in grey cast iron and special materials

Vertical submersible motor pump set for wet installation, single-stage, with three-phase motor to IEC standards. Temperature sensor for protection against overheating, optional leakage sensor in the motor space, power cable with resin-sealed, absolutely water-tight cable entry and service-friendly plug-type connection in the motor space.

Pump set:

Make:						KSB

Type:						Amarex ARX D-max

Impeller:						Open two-vane impeller D-max

D-max is an open two-vane impeller of the latest generation. The D-max impeller ensures a non-clogging flow and an excellent hydraulic efficiency.

The D-flector technology is specially designed to drastically reduce the risk of clogging by items such as wet wipes contained in the waste water.

Impeller diameter:				180				mm

Operating data:

Fluid handled:					Waste water containing faeces

Flow rate:					100				m³/h

Head:						8				m

Power input:					1.78				kW

Operating temperature:				max. 40				°C

Drive:

Nominal voltage:					400				V

Nominal frequency:				50				Hz

Starting method: 					DOL / star-delta starting is also possible

Enclosure: 					IP68 to EN 60529 / IEC 529, thermal class H

Explosion protection: 				ATEX II 2G Ex db h IIB T4 Gb / without

Max. fluid temperature: 				40 °C

Thermal motor protection:	                                Temperature bimetal switch

Leakage sensor in the motor space:		Yes / No

Efficiency class: 					Equivalent IE3 to IEC standard / Not specified

Duty type:					S1 submerged / S1 with motor partially outside the fluid

Nominal motor power P2:				2.3				kW

Nominal motor power P1:				2.6				kW

Motor efficiency:					82.6				%

Nominal current:					5.5				A

Speed:						1430				rpm

Cable length:					10				m

Cable entry:		Screwed cable entry / Cable entry with individually stripped, resin-embedded cores and service-friendly plug-type connection inside the motor

Materials:

Pump casing: 					EN-GJL-250

Handle:						1.4306

Impeller:	EN-GJS-600-3 / EN-GJN-555[CR14]

Discharge cover:	 				EN-GJL-250 / EN-GJN-555[CR14]

Suction cover:					EN-GJS-600-3 / EN-GJN-555[CR14]

Shaft:						1.4021 + QT800

Cable sheath:					Chloroprene rubber / TEFZEL

Elastomers: 		Nitrile rubber (NBR)/ encapsulated seal (FEP/FKM) / fluorocarbon rubber (FPM) = Viton

Coating:						Two-component high-solid epoxy resin

Colour:						RAL 5002

Shaft seal:

2 independent mechanical seals fitted in an oil reservoir

Pump-end:	Bellows-type mechanical seal / Mechanical seal with covered spring SiC-SiC

Motor-end:					Bellows-type mechanical seal, Carbon-AI2O3

Oil fill:						Environment-friendly, non-toxic oil

Dimensions and connections:

Nominal diameter, discharge side:			DN 80, drilled to EN 1092-2 PN 16

Nominal diameter, suction side:			DN 80, unmachined / drilled to EN 1092-2 PN 16

Net pump weight approx.:			78			kg

Installation parts:

Installation depth					4.5 / 6			m

From lower manhole edge to pump sump bottom

Stationary installation

- Duckfoot bend for guide wire arrangement

Consisting of duckfoot bend, mounting bracket, 10 m guide wire, screws/bolts and anchor bolts

Spacer for installation depth > 4.5 m

- Duckfoot bend for single guide rail arrangement

Consisting of duckfoot bend, mounting bracket, screws/bolts and anchor bolts (guide rail supplied by the operator)

Additional mounting bracket, middle support for installation depth > 6 m

- Duckfoot bend for twin guide rail arrangement

Consisting of duckfoot bend, mounting bracket, screws/bolts and anchor bolts (guide rails supplied by the operator)

Additional mounting bracket, middle support for installation depth > 6 m

Transportable model

- Feet / foot plate, complete

Lifting equipment:

-Short-linked chain, tested and marked to Directive 2006/42/EC (Machinery Directive), hook, shackle

Length:						5/10			m

Max. load					200			kg

Materials:

Claw:						EN-GJL-250 + U-profile joint NBR/Viton

Duckfoot bend (stat.): 				EN-GJL-250

Feet and plate (transp.):				1.4301

Chain:						1.4404

Electrical accessories:

-Thermistor protection relay			Yes / No

Pump without explosion protection

-Thermistor protection relay			Yes / No

Pump with explosion protection

-Leakage sensor protection relay			Yes / No

Typical tender for Amarex D-max

2573.521/02-EN

Subject to technical modification without prior notice

17.09.2020