BOA-Control SBV DN 15 - 50:

Short text:

Maintenance-free soft-seated Y-pattern balancing and measurement valve, continuous presetting, with position indicator readable from all angles (360°), travel stop and 2 measurement ports with fixed measuring orifice.

Manufacturer/Type:		KSB/BOA-Control SBV

Pressure class:	PN 25

Nominal size:	DN 15 - 50

Long text:

KSB balancing and measurement valve BOA-Control SBV, PN 25, DN 15 - 50, internal thread (½ - 2 inches)

Maintenance-free soft-seated Y-pattern balancing and measurement valve for heating and air-conditioning systems and industrial plants. Continuous presetting, with position indicator readable from all angles (360°). Includes travel stop and 2 measurement ports with fixed measuring orifice (tolerance +/- 5 %) for measuring pressure, differential pressure and flow. Minimum space requirements thanks to non-rising handwheel and all functional parts being positioned on the same side as the handwheel. Installation in supply and return, threaded ends with internal thread to ISO 288.

Manufacturer/Type:		KSB/BOA-Control SBV

Typical tender for BOA-Control SBV DN 15 - 50

7130.521/01-EN
Subject to technical modification without prior notice

23 March 2021