BOA-Control DPR threaded ends DN 15 - 50:

Short text:

Proportional control valve for the constant control of an adjustable differential pressure setpoint without auxiliary energy, setpoint continuously adjustable and readable from the outside at any time. Valve closes automatically with rising pressure, with flushing function.

Manufacturer/Type:		KSB/BOA-Control DPR

Pressure class:	PN 25

Nominal size:	DN 15 - 50

Long text:

KSB differential pressure control valve BOA-Control DPR,

PN 25, DN 15 - 50, internal thread (G ½ - 2), LP Delta P 5 - 60 kPa/HP Delta P 20 - 60 kPa

DN 15 - 50

Proportional control valve for the constant control of an adjustable differential pressure setpoint without auxiliary energy for heating and air-conditioning systems. Setpoint continuously adjustable and readable from the outside at any time. Valve closes automatically with rising pressure, with flushing function. Body made of brass (CW602N-M), threaded ends with internal thread to ISO 228, O-rings made of EPDM, with G 1/8-inch connection nipples and quick-measurement ports for measuring the pressure loss. With a filling and draining set as an optional accessory.

DN 15 (internal thread G ½) to DN 25 (internal thread G 1), PN 25

Available in nominal sizes DN 15 - 25 as a Low-Pressure version (setpoint 5 - 30 kPa) and as a High-Pressure version (setpoint 20 - 60 kPa) including shut-off function and pulse line (1 m).

DN 32 (internal thread G 1¼) to DN 50 (internal thread G 2), PN 16

Available in nominal sizes DN 32 - 50 with a setpoint range of 20 - 60 kPa (DN 50: up to 80 kPa) and tamper-proof operation using Allen key. Pulse line (1 m or 2 m) with G1/8-inch connection nipples available as an accessory.

Can be used in combination with the BOA-Control SBV balancing valve (DN 15 - 50).

Manufacturer/Type:		KSB/BOA-Control DPR

Typical tender for BOA-Control DPR DN 15 - 50, threaded ends

7137.521/01-EN
Subject to technical modification without prior notice

23 March 2021