BOA-Control DPR flanged ends DN 65 - 100:

Short text:

Proportional control valve for the constant control of an adjustable differential pressure setpoint without auxiliary energy, setpoint continuously adjustable and readable from the outside at any time. Valve closes automatically with rising pressure.

Manufacturer/Type:		KSB/BOA-Control DPR

Pressure class:	PN 16

Nominal size:	DN 65 - 100

Long text:

KSB differential pressure control valve BOA-Control DPR,

PN 16, DN 65 - 100, LP Delta P 20 – 160 kPa / HP Delta P 80 - 160 kPa

DN 65 - 100

Proportional control valve for the constant control of an adjustable differential pressure setpoint without auxiliary energy for heating and air-conditioning systems. Setpoint continuously adjustable and readable from the outside at any time. Valve closes automatically with rising pressure. Includes quick-measurement ports for measuring the pressure loss and a pulse line (2 m) with G 1/8-inch connection nipples. Also with a filling and draining set as an optional accessory. Available in nominal sizes DN 65 - 100 as a Low-Pressure version (setpoint 20 - 80 kPa) and as a High-Pressure version (setpoint 80 - 160 kPa). Body made of EN-GJL-250 (5.1301) with a maintenance-free stem seal made of EPDM, flanged ends to DIN EN 1092 PN 16 and face-to-face length to DIN EN 558-1, standard series 1.

Manufacturer/Type:		KSB/BOA-Control DPR

Typical tender for BOA-Control DPR DN 65–100, flanged ends

7137.522/01-EN
Subject to technical modification without prior notice

23 March2021