BOA-Control PIC, flanged ends DN 65 - 150:

Short text:

Pressure-independent control valve, comprising a continuously adjustable flow controller and a control valve for hydraulic balancing and dynamic volume flow control at constant valve authority. Continuous adjustment of the volume flow setpoint directly at the valve thanks to the digital scale, with mechanical locking function. With measurement ports for determining flow rate, temperature and pressure loss.

Manufacturer/Type:		KSB/BOA-Control PIC

Pressure class:	PN 16

Nominal size:	DN 65 - 150

Long text:

Pressure-independent BOA-Control PIC for balancing and controlling,

PN 16, DN 65 - 150, 4.4 - 160 m3/h

DN 65 - 150

Pressure-independent control valve, comprising a continuously adjustable flow controller and a control valve for hydraulic balancing and dynamic volume flow control in heating and cooling systems (e.g. central heating systems, underfloor heating, fan coil units and cooling ceiling systems) at constant valve authority. Continuous adjustment of the volume setpoint directly at the valve thanks to the digital scale, with mechanical blocking function. With measurement ports for determining flow rate, temperature and pressure loss. Can be installed in both the supply and return. Optionally fitted with a handwheel or actuator for the electrical control of another variable such as the room temperature by adjusting the volume flow. Body made of grey cast iron EN-GJL-250 (5.1301) with a maintenance-free stem seal made of EPDM, flanged ends to DIN EN 1092 PN 16 and face-to-face length to DIN EN 558-1, standard series 1. Available in the nominal sizes DN 65 to DN 150 and with a control range of 4.4 - 160 m3/h.

Manufacturer/Type:		KSB/BOA-Control PIC

Available actuators:

Continuous-action / 3-point actuators 24 V

Electric actuator EMV213/145

Electric actuator for BOA-Control PIC, DN 65 - 100, continuous-action / 3-point, 24 V AC/DC

Electric actuator EMV213/148

Electric actuator for BOA-Control PIC DN 125 - 150, continuous-action / 3-point, 24 V AC/DC

3-point actuators 230 V

Electric actuator EMV213/147

Electric actuator for BOA-Control PIC, DN 65 - 100, 3-point, 230 V AC

Electric actuator EMV213/150

Electric actuator for BOA-Control PIC, DN 125 - 150, 3-point, 230 V AC

Typical tender for BOA-Control PIC DN 65 - 100, flanged ends

7138.522/01-EN
Subject to technical modification without prior notice

23 March 2021