ECOLINE GT 40

Short text:

Metal-seated gate valve with flexible wedge, with gland packing and non-rotating stem, straight-way pattern, with handwheel, body made of 1.0619 (GP 240 GH),

with flanged ends to DIN EN 1092-1 or butt weld ends to DIN EN 12627,

Model with flanged ends:  face-to-face length to EN 558-1/15 (PN 10 - 25) or EN 558-1/26 (PN 40),

Model with butt weld ends:  face-to-face length to EN 12982/15 (PN 10 - 25) or EN 12982/26 (PN 40).

Manufacturer/Type :

KSB/ECOLINE GT 40

Pressure class:	PN 10 - 40

Nominal size :	DN 50 - 600

Long text:

Metal-seated gate valve with flexible wedge, with gland packing and non-rotating stem, straight-way pattern, with handwheel, body made of 1.0619 (GP 240 GH),

with flanged ends to DIN EN 1092-1 or butt weld ends to DIN EN 12627.

Model with flanged ends:  face-to-face length to EN 558-1/15 (PN 10 - 25) or EN 558-1/26 (PN 40),

Model with butt weld ends:  face-to-face length to EN 12982/15 (PN 10 - 25) or EN 12982/26, weld end design with connection branch extensions made of forged steel, stem made of 13% chrome steel with back seat, graphite gland packing with packing end rings, fully confined bonnet gasket made of graphite (PN 40), threaded bush free from non-ferrous metals, body seating surfaces hard-faced with Stellite as standard. Designed, manufactured, tested and marked in accordance with the European Pressure Equipment Directive.

For use in potentially explosive atmospheres, Group II, category 2 (zones 1 and 21) and category 3 (zones 2 and 22) to ATEX 2014/34/EU.

Manufacturer/Type:		KSB/ECOLINE GT 40

Pressure class:	 PN 10 - 40

Nominal size:	DN 50 - 600

Variants:

Stem protecting tube

or

stem protecting tube with position indicator

or

stem protecting tube with limit switch

or

bypass

or

installation kit for electric actuators to EN ISO 5210, Typ A

or

with electric actuator

or

with spur or bevel gear

or

TA-Luft-compliant to VDI 2440

or

other flange designs

or

other butt weld end designs

Typical tender for ECOLINE GT 40

7367.521/01-DE
Subject to technical modification

without prior notice

16.04.2021