NORI 40 ZXL/ZXS

Short text:

Metal-seated globe valve in straight-way pattern, with gland packing and rotating stem,

model with flanged ends: face-to-face length to EN 558-1/1,

DN 10 - 40 body made of 1.0460 (P 250 GH), DN 50 - 400 made of 1.0619+N (GP 240 GH+N)

model with butt weld ends: face-to-face length to EN 12982/64

DN 10 - 50 body made of 1.0460 (P 250 GH), DN 65 - 350 made of 1.0619+N (GP 240 GH+N),

Manufacturer/Type:		KSB/NORI 40 ZXL/ZXS

Pressure class:	PN 25/40

Nominal size:	DN 10 - 400

Long text:

Metal-seated globe valve with gland packing and rotating stem,

model with flanged ends: face-to-face length to EN 558-1/1,

DN 10 - 40 body made of 1.0460 (P 250 GH), DN 50 - 400 made of 1.0619+N (GP 240 GH+N)

model with butt weld ends: face-to-face length to EN 12982/64

DN 10 - 50 body made of 1.0460 (P 250 GH), DN 65 - 350 made of 1.0619+N (GP 240 GH+N),

-10 to + 450 °C, straight-way pattern, rotating stem made of 1.4021 with back seat, fully confined bonnet gasket, with handwheel, stem sealed by gland packing. Designed, manufactured, tested and marked in acc. with the European Pressure Equipment Directive. For use in potentially explosive atmospheres, Group II, category 2 (zones 1 and 21) and category 3 (zones 2 and 22) to ATEX 2014/34/EU.

Manufacturer/Type:		KSB/NORI 40 ZXL/ZXS

Pressure class:	PN 25/40

Nominal size:	DN 10 - 400

Variants:

with throttling plug

or

with position indicator

or

with balanced plug

or

with locking device

or

combined non-return / shut-off valve

or

studs and nuts made of A4-70 (low-temperature steel)

or

with PTFE gland packing

or

oil and grease-free

or

other types of flange or weld end designs

Typical tender for NORI 40 ZXL/ZXS

7621.521/01-EN
Subject to technical modification without prior notice

19 April 2021